## Slide 1: Arduino Workshop
Session 1

## Slide 2: At first, Let me know what do you expect from this workshop?

## Slide 3
GENIUS!

## Slide 4: Workshop Outlines
Arduino IDE
Programming basics
Basics of electrical/electronics circuits
Sensors
Motors & motor dives
Wireless control
LCD

## Slide 5: Embedded Systems

## Slide 6: Embedded Systems
An embedded system is a system that includes hardware and software combination to reach a specific target.
For example:
  Camera , iPod, older types of mobile phones, Arduino ..etc

## Slide 7: Embedded Systems
Why do we need embedded systems?
  Before embedded systems all the circuits designed were fixed.
After microcontrollers now you can have unlimited no. of changes on circuits without soldering or any changes on circuit configuration.

## Slide 8: Embedded Systems
Microcontrollers
  Simply it’s like a processor with a built-in RAM.

## Slide 9: Embedded Systems
Chips based on Microcontroller:
Arduino
Galileo
Raspberry Pi

## Slide 10: Arduino Uno

## Slide 11
Open Source Hardware
Open source
software
inexpensive
Suitable for
Windows, Linux and Mac OS
support
simple
Arduino

## Slide 12: What’s on the UNO board?

## Slide 13: Digital Signal
A Digital Signal on the Arduino can be only in two states: HIGH or LOW.
This is true whether the digital signal is an input or an output. When a pin is at 5v it is considered HIGH, and when it is at 0v or GND, it is considered LOW.

## Slide 14: Digital Inputs
Note: Sometimes a Digital Input Signal might not always have a full 5v available, so the threshold to drive an input pin HIGH is around 3v, and anything below this threshold is considered to be LOW.
And that’s why Analog i/o is more accurate.

## Slide 15: Analog Signal
We have established that a digital I/O signal must either be LOW (0v) or HIGH (5v).
Analog voltages can be anywhere in between (2v, 3.4v, 4.6v, etc.)

## Slide 16: Why should we convert A to D?
There is no device that can produce an accurate analog signal.
As it needs a tends-to-infinity size of memory
So, we convert it to a close enough digital signal

## Slide 17: Analog OUTPUT (PWM)
This is not technically an analog output, but it is the digital equivalent to an analog voltage available at an output pin.
This feature is called ‘Pulse Width Modulation’, and is an efficient way of delivering a voltage level that is somewhere between the Source and GND.

## Slide 18: Analog and Digital i/o functions
Analog
Analog INPUT
analogRead ( Pin number );
Ex: analogRead ( A0 );
Analog OUTPUT
analogWrite (PWM pin number, 0255);
Ex: analogWrite ( 3, 125 );
Digital
Digital INPUT
digitalRead ( Pin number );
Ex: digitalRead ( 2 );
Digital OUTPUT
digitalWrite ( Pin number , HIGH or LOW );
Ex: digitalWrite ( 4 , LOW );

## Slide 19: Other important Functions:
pinMode
  pinMode(Pin number, INPUT or OUTPUT);
  Ex : pinMode(2,INPUT);
delay
  delay(time in ms);
  The Arduino changes nothing for that while

## Slide 20: 1st project: Blinking an LED:
Simulator

## Slide 21: Coding Principles

## Slide 22: If statement
if ( condition is true)
{
do something;
}
else if (another condition is true)
{
do something else;
}
else
{
do something else;
}

## Slide 23: while loop
while ( condition is true)
{
do something;
}
do
{
something;
}
while ( condition is true);

## Slide 24: while VS do.. while

## Slide 25: For loop
for( counter initial value ; repeat the loop while ; counter increment/decrement)
{
// what to do in each loop/time ;
}
Example:
for( int counter = 0 ; counter < 5 ; counter = counter + 1)
{
// what to do in each loop/time ;
}

## Slide 26: Serial monitor:
Used to print output to the user

## Slide 27: Interfacing

## Slide 28: Temperature sensor
LM35 sensor
Circuit

## Slide 29: Application:
Automatically Controlling
air-conditioning system

## Slide 30: Light sensor
LDR = Light Dependent resistance
Also known as: Photo resistor = photo cell

## Slide 31: Light sensor
Circuit:

## Slide 32: Light sensor
Code:

## Slide 33: WIRELESS CONTROL
1- remote controller
2- Bluetooth module

## Slide 34: Bluetooth module
Switching led using your phone

## Slide 35: LCD
Liquid Crystal Display:

## Slide 36: LCD

## Slide 37: LCD
Note:
lcd(rs,e,d4,d5,d6,d7)

## Slide 38: LCD with I2C:

## Slide 39: Any Questions..?

## Slide 40: Thank You